Implementation of the protocol for radio link communication lab03.
We used the genfsk protocol to connect two boards with each other. We are using 2 operational codes, one for transmit and one for receive. In the protocol we take the right 8 bits of the payload and we use it in packet index. We also take the left 8bits of the payload and we use it in 16bit u16PacketIndex. We have to type cast it using uint8_t because PacketIndex takes unsigned integers. We use two operation codes, opcode1 and opcode 2 to check if we are transmitting and receiving at the same time. This is checked in an if statement and the important thing is that if (gRadioOpcode1&&gRadioOpcode2) does not apply then connection is aborted and everything goes to RF buffer. Protocol starts again from scratch. That was the original implementation of the example
What we changed: In genfsk_defsh.h line 12 we define #define TX or #define RX. That means we make one board either a transmitter or a receiver. We also added #define DEVICEADDRESS 2.That means we can define the address of a board as a constant, i.e. 2 and use it in the code, thus simplifying the case statement. In the ppp-webserver.c file we use it to give addresses to different boards, starting from 1. We’ve tested it up to 3 boards with success.
In the end we check that (if(gGenfskSuccess_c != GENFSK_StartTx(mAppGenfskId, gTxBuffer, buffLen, GENFSK_GetTimestamp() + miliSecDelay). If gGenfsk is not a success we terminate connection the and we send a message that Radio TX failed. Then the system returns to gRadioTxStateIdle_c(Idle state, not transmitting anything).
Major changes: 1) In line 185 genfsk.c ledstate is now 8bit instead of 16bits. Static uint8_t ledstate is used. It is static because we want it to hold the previous ledstate value.
2) Now the variable address is static uint8_t address, i.e. it is only 8bits instead of 16bits and we use static so the previous address value is saved. So in the latest version we don’t shift any bits right, we just send an 8bit bitstream with the address in line 293 in bool_t Genfsk_Send(). So the the declaration of the function was overload by one variable uint8_t address.

Objervation: If we click too quickly on a toggle led button, sometimes one board’s light turns off. But if we press it again it self corrects, so not a major issue. If we had more than 2 boards we could see if the issue remains. Is it a package loss or just a glitch? Somehow it doesn’t seem to receive it in the beginning, but when you send the data again it seems to receive it. This could be fixed with two additions to the code. Firstly, if we had more time we would have added acknowledgements to the ppp-webserver.c code. For example in line 507 after Genfsk_Send(gCtEvtTxDone_c, NULL, ledState1,1); we could have added a send acknowledgment. Simple one-way ACK to be received after we send the ledState and the DEVICEADDRESS. We could do a dual way ACK so we could have one acknowledgement to confirm the send and one ACK sent by the receiving board, to account for packet loss.
The safest way to test packet loss is to create a handshake protocol ,even before the sender sends his first packet through Genfsk_Send function. This could be done with a three-way handshake protocol similar to TCP. We would need 1 bit for SYN (establishing that we have synchronization between Host A and B, an two more ACKs. In detail:
Host A sends a SYNchronize packet to Host B
Host B receives A's SYN
Host B sends a SYNchronize-ACKnowledgement //1ST ACK I mentioned
Host A receives B's SYN-ACK //1st ACK received by B
Host A sends ACKnowledge //2nd ACK sent by host A
Host B receives ACK.  //2nd ACK received by host B
Socket connection is ESTABLISHED. // Handshake complete, connection established.
This simple protocol would prevent data loss and would have a synchronized connection between HostA and HostB, let’s say TX transmitter and RX receiver. Every packet sent would be accounted for due to the double ACKs used. If a packet was lost we could use a 16bit buffer and forward all the packets to the buffer while the other packets kept being forwarded. After the buffer was full the 16bit packets would be sent. I assume that each packet is 1 bit. We could even use an algorithm to handle the buffer size if we wanted such as Random early detection (RED). By using a counter for the average queueLength we could drop packets with high probability or enqueue them in our 16bit queue. This would really help if we toggled the lights very quickly, as we believe that issue was caused due to overflow of the 16bit buffer u16PacketIndex, so theoretically we would have no data loss
Comment :Led2 is red, LED3 is green, LED4 blue
Genfsk.c line 228 // We check the device address of the board. If ledstate is 1 we turn the LED3 on. Else it is off.
In ppp-webserver.c when we press the button we request a wepage. Here I have 3 webpages. If the first button is pressed we request webpage with char ‘a’, we turn led2 on and ledstate is 1. Address is 1. If the Toggle LED2 is pressed , ledstate1 is updated to ledstate2 and board address is 2. Led3Toggle() function turns LED3 on, i.e. green. Lastly pressing ToggleLED3 button sends a get request for the webpage. Led status is updated from 2 to lestate3 and board address is now 3. We toggle LED4 ,so we see a blue light on the board.
We changed the shifting. Now we use 8 bit for the address , 8bits for the ledState and we only use 8bits in the payload for either TX or RX. We need ledState because we check if address and ledState are in sync. Line 293, function Genfsk_Send we just used an uint_8t ledState and an uint_8t for the address as parameters in the function).